# FABLINE CLEANROOM DOOR MODULES

# SECTION 1 GENERAL

# 1.01	PRODUCT NAME

- FabLine Cleanroom Door Modules

# 1.02	MANUFACTURER

A.	Porta-Fab Corporation

18080 Chesterfield Airport Road

Chesterfield, MO  63005 U.S.A.

Phone:	(636) 537-5555

Fax:	(636) 537-2955

- The use of a manufacturer's name, model or catalog number is for the purpose of establishing the standard of quality and general configuration.

# 1.03	PRODUCT DESCRIPTION

Basic Uses:  The FabLine Cleanroom Door Modules are designed to add the same protection, strength and reliability to a new or existing cleanroom, ensuring performance geared to the expectations for which the cleanroom is being installed.  The door modules shall install within a framework providing a gasketed seal at the door and frame connection. The FabLine Cleanroom Door Modules are designed for use in environments up to a sub-M1 classification where maximum performance, strength and reliability are required. The doors are designed for environments within the microelectronics industry and all supporting and related industries.

- Cleanroom Door Modules:

- Materials:

- All jambs and headers shall be of aluminum alloy 6063-T5 within commercial tolerance and free from defects impairing strength and/or durability.  Door stile and rail sections to be a minimum 1/8" wall thickness.

- Steel tension rods of .375 inch diameter shall run the full width of the top and bottom rails and shall be fixed with steel plates and lock nuts.

- Hardware Options:

- Top and bottom pivots

- Push bar

- Pull handle

- 1/2" x 4" threshold

- Deadbolt MS lock

- Lock faceplate

- Surface mount closer

- Concealed door closer

- Flush bolts (double doors)

- Special hardware for custom doors shall be specified by the architect.

- Panel Options: Full panel or half panel doors shall be glazed with either of the following:

- Glass Panel: 1/4" tempered safety glass as specified.

- Solid Panel: Panels shall be .032" smooth aluminum with a smooth conductive epoxy finish laminated to both sides of an aluminum honeycomb core.  Wall panel shall have a surface resistivity in the range of 106 to 109 ohms/square per EOS/ESD-S11.11-1993, which supersedes ASTM-D257, and an electrostatic decay of <10% IN, .5/sec. per method 4066 Federal Test Method Standard 101B.

- Colors:	As selected by the Owner from manufacturer's standard panel color.

- Finish:

- All exposed framing surfaces shall be free of scratches and other serious blemishes.

- Finish to be: Etched and clear anodized

End of Section